## Slide 1: SmartGreenHouse
Tommaso Giorgi

## Slide 2: Introduction
Different sensor can be used inside a greenhouse. Monitoring them can help the appearance and shape, material metabolism, growth and development, quality, and yield of plants.
Data that can be monitored:
Temperature
Humidity
Soil PH
Soil Moisture
Light

## Slide 3
System Architecture
Two sensors networks have been used:
MQTT Network
  Humidity + (De)Humidifier
  Temperature + Heater/Air Conditioner
COAP Network
  Light Sensor
  Soil PH + Automatic Fertilizer
  Soil Moisture + Irrigation System
Data are collected from the border router and sent to the Java Application (Collector)
The collector stores data on a MySQL database and exposes a CLI with commands that can be used to perform different actions with the sensors

## Slide 4: COAP
Soil PH
Correct range
/soilph/sensorph
  GET: retrieve the current soil ph value
  EVENT: we want to notify observers about change of the sensor (change over time to simulate real behaviour)
/soilph/fertilizer
  PUT quantity=<0,1,2,3>
  Turn on or off the fertilizer with the specified quantity
Soil Moisture
/soilmoisture/moisture
  GET: retrieve the current soil moisture value
  EVENT: we want to notify observers about change of the sensor (change over time to simulate real behaviour)
/ soilmoisture /irrigation
  PUT mode=<ON,OFF>
  Turn on or off the Irrigation System
Light
/light/light
  GET: retrieve the current light intensity value
  PUT intensity=<0,1,2>
  Turn on or off the lights with the specified intensity
Intensity = 0
Intensity = 1
Intensity = 2

## Slide 5: MQTT
Humidity
humidity_s [TOPIC]
  Topic in which the different values of the humidity are posted
humidity_act [TOPIC]
  Topic used for commands:
  ON_DEH: Turn on Dehumidifier
  ON_HUM: Turn on Humidifier
  OFF: Turn off all the actuators
Temperature
temperature [TOPIC]
  Topic in which the different values of the temperature are posted
actuator [TOPIC]
  Topic used for commands:
  ON_REF: Turn on Refrigerator
  ON_HEA: Turn on Heater
  OFF: Turn off all the actuators

## Slide 6: Data Encoding
{
node_id = “nodeID”,
moisture_value = 1.48
}
{
node_id = “nodeID”,
ph_value = 8.37
}
{
node_id = “nodeID”,
humidity = 50
}
{
node_id = “nodeID”,
temperature = 24
}
All sensors return the data they have collected in JSON format:
JSON is lighter (less verbose and more flexible)
Better with little batteries devices
Non-text based format not fully supported on Contiki